## Slide 1: Recitation 8: Exam Stack Review 15-213: Introduction to Computer Systems October 17th, 2016
Instructor:
Your TA(s)

## Slide 2: Midterm Exam This Week
4 hours
1 double-sided page of notes
  No preworked problems from prior exams
7 questions
Report to the room
  TA will verify your notes and ID
  TAs will give you your exam server password
  Login via Andrew, then navigate to exam server and use special exam password

## Slide 3: Stack Review
In the following questions, treat them like the exam
  Can you answer them from memory?
  Write down your answer
  Talk to your neighbor, do you agree?
Discuss: What is the stack used for?

## Slide 4: Stack Manipulation
We execute:
      mov $0x15213, %rax pushq %rax
Which of the following instructions will place the value 0x15213 into %rcx?
      1) mov (%rsp), %rcx
      2) mov 0x8(%rsp), %rcx
      3) mov %rsp, %rcx
      4) popq %rcx
Notes: OBJECTIVE: RSP points to the newest value on the stack

## Slide 5: Stack is memory
We execute:
      mov $0x15213, %rax pushq %rax
      popq %rax
If we now execute: mov -0x8(%rsp), %rcx what value is in %rcx?
1) 0x0 / NULL
2) Seg fault
3) Unknown
4) 0x15213
Notes: OBJECTIVE: popping a value does not remove it from the stack

## Slide 6: x86-64 Calling Convention
What does the calling convention govern?
1) How large each type is.
2) How to pass arguments to a function.
3) The alignment of fields in a struct.
4) When registers can be used by a function.
5) Whether a function can call itself.
Notes: 1-4 are all part of the ABI, only 2 and 4 are calling convention

## Slide 7: Register Usage
The calling convention gives meaning to every register, describe the following 9 registers:
%rdi
%rsi
%rdx
%rcx
%r8
%r9
%rax
%rbx
%rbp
Function Argument
Return Value
Callee Save

## Slide 8: Register Usage
The calling convention gives meaning to every register, describe the following 9 registers:
%rdi
%rsi
%rdx
%rcx
%r8
%r9
%rax
%rbx
%rbp
Function Argument
Return Value
Callee Save
4
3
2
1
5
6

## Slide 9: Register Usage
Which line is the first violation of the calling convention?
mov $0x15213, %rax
push %rax
mov 0x10(%rsp), %rcx
mov %rbx, %rax
pop %rdx
push %rax
pop %rbx
mov %rcx, %rbx

## Slide 10: Register Usage
Which line is the first violation of the calling convention?
mov $0x15213, %rax
push %rax
mov 0x10(%rsp), %rcx
mov %rbx, %rax
pop %rdx
push %rax
pop %rbx
mov %rcx, %rbx
Until this point, the callee has preserved the callee-save value.

## Slide 11: Sometimes arguments are implicit
How many arguments does “rsr” take?
How many registers are changed before the function call?
(Note, %sil is the low 8 bits of %rsi)
0x0400596 <+0>: cmp %sil,(%rdi,%rdx,1)
0x040059a <+4>: je 0x4005ae <rsr+24>
0x040059c <+6>: sub $0x8,%rsp
0x04005a0 <+10>: sub $0x1,%rdx
0x04005a4 <+14>: callq 0x400596 <rsr>
0x04005a9 <+19>: add $0x8,%rsp
0x04005ad <+23>: retq
0x04005ae <+24>: mov %edx,%eax
0x04005b0 <+26>: retq

## Slide 12: Arguments can already be “correct”
rsr does not modify s and t, so the arguments in those registers are always correct
int rsr(char* s, char t, size_t pos)
{
if (s[pos] == t) return pos;
return rsr(s, t, pos - 1);
}

## Slide 13: Recursive calls
Describe the stack after doThis(4) returns.
void doThis(int count)
{
char buf[8];
strncpy(buf, “Hi 15213”, sizeof(buf));
if (count > 0) doThis(count – 1);
}
push %rbx
sub $0x10, %rsp
mov %edi,%ebx
movabs $0x3331323531206948,%rax
mov %rax,(%rsp)
...